## Slide 1
GPU Architecture for Inference
Sizing the box with arithmetic, not benchmarks · NVIDIA Partner Lab Series · Lab 04
Notes: Welcome. This is the analytical lab: no GPU required, no NIM calls — every number comes
from datasheet tables and a back-of-the-envelope capacity model. The throughline is
that 'H100 is 6× faster than A100' is true for exactly one workload regime and
misleading for several. By the end you'll defend a GPU SKU and a count with arithmetic.

## Slide 2
Agenda & learning objectives
• The problem: defend a GPU sizing decision to procurement
• HBM: capacity vs bandwidth, and the two ways you run out
• A step-by-step walkthrough of every notebook exercise — with worked examples
• By the end you will be able to:
  – Compute the KV-cache tax per token and the concurrency ceiling it sets
  – Explain why decode is memory-bound and prefill is compute-bound
  – Find the roofline crossover batch and read it off a throughput curve
  – Turn a target RPS + SLA into a GPU count with a capacity planner
Notes: This lab is heavy on intuition and arithmetic. The two results that reshape real
deployments: the roofline crossover batch (where 'more FLOPs' stops helping decode) and
the moment a 70B model simply won't fit on one GPU. Promise them they'll leave able to
turn a vendor claim into a defensible config.

## Slide 3
The Problem
Notes: Anchor in a budget review, not abstract specs.

## Slide 4
The scenario — sizing a multi-tenant LLM service
• An ML engineer is sizing GPU infra; budget review is Thursday
• The vendor deck says 'H100 is 6× faster than A100'
  – true for one workload regime, misleading for several others
• Procurement wants one SKU and a GPU count
  – The engineer needs to defend it with arithmetic, not a benchmark screenshot
Every number in this lab comes from the datasheet tables in data/
Notes: Make the '6×' claim concrete and then promise to dismantle it: it's real only when
decode is compute-bound, and most chat traffic isn't. The deliverable procurement wants
is a single number — GPUs — and the lab builds the model that produces it defensibly.

## Slide 5
HBM — two numbers, two ways to run out
• HBM (High Bandwidth Memory) = the GPU's on-package video memory
  – the memory_gb in the specs (e.g. 80 GB on an H100)
• Capacity (memory_gb) — HOW MUCH FITS: weights + KV cache both live here
• Bandwidth (mem_bandwidth_gb_s) — HOW FAST you can read it
  – decode rereads every weight per token, so token speed tracks bandwidth
Capacity (weights+KV) is a SIZE problem; decode speed is a BANDWIDTH problem
Notes: This one-liner carries the whole lab. The two HBM numbers map to the two failure modes:
capacity problems ('70B won't fit', concurrency ceiling) and bandwidth problems (slow
single-user decode). Keep coming back to 'size vs speed' — students who internalize it
predict the rest of the lab.

## Slide 6
The Roofline
Notes: Decode and prefill live on opposite sides of it.

## Slide 7
Decode vs prefill — two sides of the roofline
• Decode (generate one token): reread every weight from HBM, do ~2×params FLOPs
  – ~1 FLOP/byte → tensor cores idle, waiting on memory → MEMORY-bound
• Prefill (process the prompt): 2×params FLOPs for every input token at once
  – high arithmetic intensity → COMPUTE-bound (FLOPs and FP8 matter here)
• Single-user token speed tracks bandwidth; TTFT tracks FLOPs
The same GPU lives on BOTH sides of the roofline within one request
Notes: This is the conceptual heart. Decode is bandwidth-starved at small batch because it does
almost no math per byte read; prefill is the opposite. So a chatty short-prompt workload
is decode-heavy (wants bandwidth) and a long-context RAG/summarize workload is
prefill-heavy (wants FLOPs/fp8). The roofline is just min(memory ceiling, compute
ceiling), and where they cross is the ridge we compute in exercise 3.

## Slide 8
Lab 04 — Notebook Walkthrough
Notes: Fully analytical. Each exercise is a small formula; the payoff is the capacity planner.
Every slide maps to a cell — have students predict each number.

## Slide 9
Lab 04 · Setup — the datasheet tables
No GPU, no NIM. Everything computes from the JSON tables in data/.
setup cell — the objects you'll use
GPUS = h100_sxm, h100_pcie, a100_80_sxm, l40s
(memory_gb, mem_bandwidth_gb_s, fp16/fp8_tflops, nvlink, $/hr)
MODELS = llama31_8b, llama31_70b
(params, num_layers, kv_heads, head_dim)
WORKLOADS = chat, rag, summarize
(target_rps, in/out tokens, ttft_ms_sla, itl_ms_sla)
MEM_UTIL = 0.90 # usable fraction of HBM after framework overhead
helpers: peak_flops(), mem_bandwidth(), weight_bytes(), dtype_bytes()
Notes: Orient them in the tables — GPUs, models, workloads. Stress fp8_tflops is null for the
A100 (sm80 can't do fp8), which the helpers handle. MEM_UTIL=0.90 is the usable HBM
fraction; everything downstream subtracts framework overhead via this.

## Slide 10
Lab 04 · Exercise 1 — the KV-cache tax per token
Every context token costs HBM: K and V vectors, at every layer.
kv_bytes/tok = 2 × layers × kv_heads × head_dim × dtype_bytes.
  – The 2 is K AND V.
Use kv_heads (GQA), NOT the full attention head count.
  – layers/kv_heads/head_dim are architecture choices — you look them up.
worked example (fp16, 2 bytes)
8B : 2 × 32 layers × 8 × 128 × 2
= 131,072 B = 128 KiB / token
70B: 2 × 80 layers × 8 × 128 × 2
= 327,680 B = 320 KiB / token
70B is 2.5× the 8B because it's 2.5× deeper
(KV scales linearly with num_layers)
Notes: This single number drives the concurrency ceiling and reappeared as the 503-causing
budget in Lab 03. The GQA point is the one to land: Llama-3.1 uses 8 KV heads to serve
32–64 attention heads, shrinking the cache 4–8×. Without GQA, long context would be
unaffordable. Note these hyperparameters are looked up from the model card, not derived.

## Slide 11
Lab 04 · Exercise 2 — HBM budget → concurrency
HBM holds weights (fixed) + KV cache (grows with concurrency).
Weights are paid first; whatever's left is your KV budget.
usable = memory_gb × 1e9 × 0.90.
kv_budget = usable − weight_bytes.
max_tokens = kv_budget // kv_bytes_per_token.
max_sequences = max_tokens // context_len.
8B fp16, context = 1280
GPU weights KV tokens max seqs
H100 80GB SXM 16.1 GB 426,788 333
A100 80GB SXM 16.1 GB 426,788 333
L40S 48GB 16.1 GB 207,061 161
weights identical; the 48GB L40S has far less
left for KV -> ~half the sequences.
Capacity here is a MEMORY story.
Notes: This is the hardware that set the Lab 03 KV ceiling. The teaching: both 80 GB cards hold
the same ~333 sequences regardless of their very different compute, while the 48 GB L40S
holds half — because concurrency is a capacity (size) problem, full stop. Compute
doesn't enter until the next exercise.

## Slide 12
Lab 04 · Exercise 3 — the decode roofline
Decode is memory-bound: read every weight, do ~2×params FLOPs.
Batching amortizes the weight read over B sequences.
memory_bound = batch × bandwidth / weight_bytes (grows with batch).
compute_bound = peak_flops / (2 × params) (flat ceiling).
tok/s = min(memory_bound, compute_bound).
crossover batch = peak_flops / bandwidth = the FLOP:byte ridge.
8B fp16 decode vs batch (H100 SXM)
crossover batch = 295 (= ridge 295 FLOP/byte)
batch 1 : 209 tok/s memory-bound
batch 32 : 6,679 tok/s memory-bound
batch 256 : 53,432 tok/s memory-bound
batch 512 : 61,613 tok/s compute-bound (ceiling)
linear climb, then a hard FLOP ceiling.
below the ridge: free throughput; above: only latency
Notes: The crossover batch equals the GPU's FLOP-per-byte ratio — the roofline 'ridge'. Below
it you're wasting compute and batching buys near-linear throughput; above it more batch
only adds latency. THIS is why '6×' is regime-specific: single-user decode tracks
bandwidth (~1.6×), saturated throughput tracks FLOPs (~3×+). We prove that in Failure 2.

## Slide 13
Lab 04 · Exercise 4 — prefill and TTFT
Before the first token, the model processes the whole prompt: prefill.
Prefill does 2×params FLOPs for EVERY input token at once.
High arithmetic intensity → COMPUTE-bound (FLOPs & fp8 matter).
ttft_s ≈ 2 × params × input_tokens / peak_flops.
Decode is a memory problem; prefill is a compute problem.
8B prefill TTFT floor (1024 input tokens)
H100 80GB SXM fp16 : 16.6 ms
A100 80GB SXM fp16 : 52.7 ms
H100 SXM fp8 : 8.3 ms
here the H100 really is ~3.2× the A100 (the FLOPs
ratio), and fp8 halves it again.
prefill = where compute headroom shows up;
decode = where bandwidth does.
Notes: This is the opposite of the decode story, and showing them back to back is the lesson:
the same two GPUs that decode at ~1.6× apart prefill at ~3.2× apart. Long-context
workloads (RAG, summarization) are prefill-heavy and benefit most from FP8 and FLOPs;
chatty short-prompt workloads are decode-heavy and benefit most from bandwidth.

## Slide 14
Lab 04 · Exercise 5 — the capacity planner (capstone)
Demand: required_tps = target_rps × output_tokens.
Batch ceiling = min(KV-cache limit, ITL-SLA limit).
  – ITL limit = itl_sla_s × peak_flops / (2 × params).
Supply: per_gpu_tps = decode_tokens_per_s(batch).
Count: num_gpus = ceil(required_tps / per_gpu_tps); check TTFT.
chat: 50 rps × 256 out = 12,800 tok/s
GPU batch bind tok/s/gpu gpus TTFT
H100 80 SXM 333 KV cache 61,613 1 16.6 OK
A100 80 SXM 333 KV cache 19,427 1 52.7 OK
L40S 48GB 161 KV cache 8,662 2 45.4 OK
chat SLA is loose, so KV cache (not latency) binds.
binding constraint decides the lever: here FP8 (smaller
weights + KV) buys a bigger batch.
Notes: The number procurement wants. Walk the chain: demand from RPS × output tokens; batch
capped by whichever is smaller — KV cache (memory) or ITL SLA (latency); supply from the
decode curve at that batch; then ceil to a GPU count and check TTFT. One H100 or A100
covers 50 rps of chat; the L40S needs two. Because KV binds, fp8 is the highest-leverage
knob — that's the challenge.

## Slide 15
Lab 04 · Failure 1 — the 70B that won't fit
Swap the 8B for the 70B and it breaks the single-GPU assumption
before throughput even enters the picture. Watch the weight-fit check.
70B weight-fit on one 80GB GPU (usable 72 GB)
70B fp16: weights 141.2 GB -> fits=False (KV headroom -69.2 GB)
70B fp8 : weights 70.6 GB -> fits=True (KV headroom +1.4 GB)
minimum tensor-parallel size to fit weights:
fp16 -> tp=2 (70.6 GB/GPU) fp8 -> tp=1 (70.6 GB/GPU)
141 GB does not fit 80 GB -> shard weights with tensor parallelism (TP).
TP reads partial activations from every peer on every layer
-> those GPUs need NVLink (900 GB/s on SXM), not PCIe.
Notes: fits_on_one_gpu=False is a hard stop, not a throughput tweak — this is the classic
capacity-planning blunder, sizing a 70B without checking weight-fit first. fp8 *just*
fits on one GPU but with 1.4 GB of KV headroom = near-zero concurrency, so the practical
floor is still tp≥2. This is why NVLink exists: TP makes GPUs talk every layer.

## Slide 16
Lab 04 · Failure 2 — buying FLOPs for a memory-bound workload
A tempting 'fix' for slow single-user decode: buy a higher-FLOP GPU.
Compare A100 vs H100 SXM at batch 1, then at saturating batch.
8B fp16 decode: A100 vs H100 SXM
batch 1: A100 127 tok/s | H100 209 tok/s -> H100 1.64×
batch 512: A100 19,427 tok/s | H100 61,613 tok/s -> H100 3.17×
FLOPs ratio H100/A100 = 3.17×
Bandwidth ratio H100/A100 = 1.64×
batch 1 (memory-bound): you only get the BANDWIDTH ratio —
the extra FLOPs sit idle. The 3.17× appears only once batching
makes decode compute-bound. Match the GPU to the regime.
Notes: This is the payoff of the roofline. At batch 1 the H100's edge is just its bandwidth
advantage (1.64×) — the FLOPs are idle. The headline 3.17× only materializes when
continuous batching pushes decode into the compute-bound region. So if the problem is
single-user latency, the high-FLOP GPU barely helps; the lever is bigger batch or more
bandwidth. That's the whole point of knowing which side of the roofline you're on.

## Slide 17
Key takeaways
• Weights first, KV with the rest — that ratio is your concurrency ceiling; GQA makes long context affordable
• Decode is memory-bound, prefill is compute-bound — same GPU, both sides of the roofline
• The crossover batch is the FLOP:byte ridge — below it batching is free, above it only latency
• Check weight-fit first — 70B fp16 (141 GB) mandates tensor parallelism + NVLink
• Size from the binding constraint — KV cache vs ITL SLA picks the batch and the lever
Notes: Recap as a checklist. The one thing to remember: name the regime before you name the
GPU. 'Faster' is meaningless until you know whether your workload is bound by memory
size, memory bandwidth, or compute — and the arithmetic here tells you which.

## Slide 18
The NVIDIA stack & references
• H100 SXM vs PCIe, HBM3, NVLink — the capacity & bandwidth specs
• GQA + KV cache, FP8 (Transformer Engine), TRT-LLM continuous batching
• MIG for multi-tenant partitioning (the 'multi-tenant' in the scenario)
  – resources.nvidia.com/en-us-tensor-core · docs.nvidia.com/tensorrt-llm/
Notes: Map the arithmetic to the real silicon and software: HBM3 bandwidth, NVLink for TP, FP8
via Transformer Engine, and continuous batching in TRT-LLM (which is how you actually
reach the high-batch compute-bound region). Hand off to the notebook capacity planner.

## Slide 19
Questions?
Then open Lab 04 — labs/04-gpu-architecture/lab.ipynb
Notes: Take questions, then move to the hands-on capacity planner. The challenge re-runs the planner with fp8 and sizes the 70B with tp.